## Slide 1: From Code to EM Signals: A Generative Approach to Side Channel Analysis-based Anomaly Detection
BY: KURT A. VEDROS
MAJOR ADVISORS: DR. CONSTANTINOS KOLIAS AND DR. MIN XIAN
SPONSORED BY: DEPARTMENT OF ENERGY (DOE) IDAHO OPERATIONS OFFICE CONTRACT, AS PART OF LABORATORY DIRECTED RESEARCH AND DEVELOPMENT (LDRD) PROGRAM OF IDAHO NATIONAL LABORATORY (INL).

## Slide 2: Side-Channel Analysis for Anomaly Detection
New type of hardware security
External
Non-nonintrusive
Cybersecurity for devices with limited resources (e.g., embedded devices)
No crypto libraries
No protection tools (antivirus software)
Emission types
Power
Thermal
Acoustic
Electromagnetic (higher bandwidth and sampling rates)

## Slide 3: Morphology of EM Signals from Embedded Devices
Produced by the EM field created when the magnetic and electrical fields interact.
  Caused by the change in flow of electrical current inside the device’s circuitry.
Amplitude Modulated by the execution of instructions
  Each instruction takes a set amount of cycles (two waves).
  It is common for each instruction to span one to three cycles (depends on the CPU type).
  Main difference is the peak amplitude values.
  Amplitudes are not static in nature
    slight variations between each run.
Base frequency modulated to that of the clock of the monitored CPU.

## Slide 4: Test Bed
Equipment
ATmega 2560 AVR MCU.
EMRSS RF Explorer H-Loop EM Probe.
Behive 150A EMC probe amplifier.
PicoScope 3403D oscilloscope.
Laptop.
Parameters.
  Sample Rate: 500 MSamples/sec
  Sampling Interval: 2nsec
  Duration: < 1 μsec

## Slide 5: Challenges of EM-based Side-Channel Analysis
Red : Clean Signal Blue: Noisy version of same signal

## Slide 6: Challenges of EM-based Side-Channel Analysis
Careful positioning of probe!

## Slide 7: Challenges of EM-based Side-Channel Analysis

## Slide 8: Challenges of EM-based Side-Channel Analysis

## Slide 9: Code-to-EM Signal Synthesis using GANs
Tokenizer
Conditional GANs
ResGANs
Wasserstein GAN with Gradient Penalty

## Slide 10: Workflow for EM-based anomaly detection

## Slide 11: Complicated due to Active Device State
Different amplitude peaks
Residual electrical charge

## Slide 12: Accounting for Active Device State
Library of instructions to signals.
Not realistic to locate and harvest signals of very large sequences
Example: ATmega2560 contains 123 executable instructions.
  Increases the total possible sequences by the power the number of prior instructions plus 1.
    Total possible sequences…
      1 prior instruction: 1232 = 15,129
      2 prior instructions: 1233 = 1,860,867
      3 prior instructions: 1234 = 228,886,641
No Influence Case
Real Case (account for prior instructions)

## Slide 13: Accounting for Active Device State

## Slide 14: Programs
Program
Benign program created from common sequences of popular Arduino ATmega 2560 programs found on Github
Applied White Gaussian Noise
Obtained 25, 20, 15 Signal to Noise Ratio (SNR) samples

## Slide 15: Evaluation of Fidelity

## Slide 16: Evaluation for Anomaly Detection

## Slide 17: Visual Comparison
Retain only first peak amplitudes
Reduces resources
Focuses model to improve performance

## Slide 18: Visual Comparison

## Slide 19: Detection Models
K-NN
lazy-learning
Simple
Decision based on the Euclidean Distance of the kth neighbor to the baseline.
  Low distance score = Normal
  High distance score = Anomalous
Autoencoder
Dimensionality reduction
Decision based on reconstruction error, (mean square error between the input and output)
  Low reconstruction error = Normal
  High reconstruction error = Anomalous

## Slide 20: Anomaly Detection

## Slide 21: Q1: What is the performance of traditional methods?
Works well in low noise level environments.
Peak performance with relatively few samples
Suffers in high noise environments.

## Slide 22: Q2: Can we improve traditional methods using AEs?
Near perfect results at 25 SNR.
Outperforms k-NN at lower SNRs.
Requires large samples (2000) to reach peak performance.

## Slide 23: Q3: Can we obtain similar results using our framework?
Similar results to when training on Real EM signals.
Still outperforms k-NN at lower SNRs.
Able to feasibly obtain large training samples.

## Slide 24: Final Conclusions
Our framework can generate synthetic signals that accurately approximate the real captured EM signals for a given program.
The synthetic signals created from our generative model can be utilized to train an EM-based anomaly detection model to the point that it outperforms other models that were trained using real signals.

## Slide 25: Future works
Transfer learning methods for accounting for changes in EM-probe, type of EM-probe, or device model.
  Domain adaptation
Different generative models for EM synthesis.
  Transformers
  Denoise Diffusion
  Space State Models (SSM) with in Deep Learning
Feature Engineering
  Improve generative performance.
    Instruction + Input values
      X2 improvement on fidelity (half the Euclidean distance)

## Slide 26: Thank you for your attention. Questions?
From Code to EM Signals: A Generative Approach to Side Channel Analysis-based Anomaly Detection
Speaker: Kurt Vedros
Email: kvedros@uidaho.edu